ABCD Matrix and q-parameter evolution
ABCD Matrix Convention
There are two conventions for the definition of (x, x').
The first one is
size 22 {x' = {dx} over {dz}}
used by Kogelnik & Lee, and Gerhard Kloos.
The other one is
size 22 {x' = n {dx} over {dz}}
used by Siegman.
K&L assumes that the input and output planes are always in the vacuum (n=1).
Siegman deals with more general cases where the input and output planes
may be in different medium.

---
q-parameter
size 22 {1 over {q(z)} = {1} over {R(z)} - i {%lambda} over {%pi w^2(z)}}
λ is always the wavelength of the light in the transmitting medium.
size 22 {%lambda = %lambda_0 over n}
At the interface of two media, the beam size should not change.
This means that the value of q must change even if it is a flat interface
plane with normal incidence.
The reduced q-parameter qr = q/n is thus convenient, because it does
not change between two media.
ABCD transformation rule
size 22 {q_2 over n_2 = {A (q_1/n_1) + B} over {C (q_1/n_1) +D}}
For q-parameter:
size 22 {q_{nitalic r2} = {A q_{r1} + B} over {C q_{r1} +D}}
For reduced q-parameter:

---
Propagation in medium with index n
size 22 {left (matrix{A # B ## C # D}right ) = left (matrix{1#L/n##0#1}right)}
size 22 {q_{r2} = q_{r1} + L/n}
size 22 {q_2 = q_1 + L}
Slanted incidence to a plane interface
size 22 {left (matrix{A # B ## C # D}right ) = left (matrix{{cos %theta_2} over {cos %theta_1} #0##0#{cos %theta_1} over {cos %theta_2}}right)}
The beam size changes between the interface.
This can be derived from a purely geometrical
consideration.
w1
Note that after a transmission of an oblique
optics, the beam becomes elliptic.
w2

---
q-parameter in gtrace
In gtrace, q-parameters of a beam are stored in five attributes.
q: average q-parameter of the beam. If the beam is elliptic, this is a q-parameter
    of a circular beam best matching the elliptic one.
qx: q-parameter of the beam in x-direction.
qrx: reduced q-parameter in x-direction. qrx = qx/n
qy: q-parameter of the beam in y-direction.
qry: reduced q-parameter in y-direction. qry = qy/n
If any of the last 4 parameters are changed, all the other related parameters are
automatically updated.
ABCD transformation is calculated with the reduced q-parameters. The result is
reflected to the normal q-parameters immediately.