gtrace
Gaussian beam ray-TRACE package
for Python
Yoichi Aso
University of Tokyo

---
Programmatically Optimize Optical Layouts

---
Useful for the main beam path
ETMY
ITMY
PRM
PR2
From MC
ITMX
ETMX
BS
PR3
SR2
SR3
SRM

---
Gaussian Beam Propagation

---
ABCD Matrix
Reflection
Refraction

---
Astigmatism
Elliptic Beams

---
Keeping Track of
Gouy phase
Optical distance
Optical Power

---
Define a Gaussian Beam Object
#q-parameter of the beam
q0 = gauss.Rw2q(ROC=np.inf, w=0.3*mm)
#Create a GaussianBeam object.
b1 = beam.GaussianBeam(q0=q0, wl=1064*nm, length=30*cm, P=1.0)
#Set the direction angle of the beam to 10deg from the global x-axis.
b1.dirAngle = deg2rad(10)
#Set the position of the origin of the beam
b1.pos = (0.0, 0.0)

---
Define a Mirror Object
M1 = opt.Mirror(HRcenter=[50*cm, 10*cm], normAngleHR=pi,
        diameter=25*cm, thickness=10*cm,
        wedgeAngle=deg2rad(0.25), inv_ROC_HR=1./(120*cm),
        inv_ROC_AR=0,
        Refl_HR=0.9, Trans_HR=1-0.9,
        Refl_AR=500*ppm, Trans_AR=1-500*ppm,
        n=1.45, name='M1')

---
Hit the Mirror
>>>beams1 = M1.hitFromHR(b1, order=2)
>>>beams1
{'input': <gtrace.beam.GaussianBeam at 0x39bab90>,
 'r1': <gtrace.beam.GaussianBeam at 0x39bae30>,
 's1': <gtrace.beam.GaussianBeam at 0x39badd0>,
 's2': <gtrace.beam.GaussianBeam at 0x39baf50>,
 's3': <gtrace.beam.GaussianBeam at 0x39d5050>,
 't1': <gtrace.beam.GaussianBeam at 0x39baef0>,
 't2': <gtrace.beam.GaussianBeam at 0x39bae90>}

---
t2
s2
r1
s3
t1
s1
input

---
Non-Sequential Trace
>>>beams = non_seq_trace([M1,M2,M3], b1,
        order=30, power_threshold=1e-6)
>>>beams
<gtrace.beam.GaussianBeam at 0x39d52f0>,
 <gtrace.beam.GaussianBeam at 0x39d5230>,
 <gtrace.beam.GaussianBeam at 0x39d50b0>,
 <gtrace.beam.GaussianBeam at 0x39bad10>,
 <gtrace.beam.GaussianBeam at 0x39d5650>,
 <gtrace.beam.GaussianBeam at 0x39d5590>,
 <gtrace.beam.GaussianBeam at 0x39d5470>,
 <gtrace.beam.GaussianBeam at 0x39d5350>,
 <gtrace.beam.GaussianBeam at 0x39d59b0>,
 <gtrace.beam.GaussianBeam at 0x39d58f0>, …

---
DXF Output
#Create a canvas object
cnv = draw.Canvas()
#Draw all beams
drawAllBeams(cnv, beams, drawWidth=True, sigma=3.0,
        drawPower=False, drawROC=False, drawGouy=False,
        drawOptDist=False, layer='main_beam',
        fontSize=0.01)
#Draw the mirror
drawAllOptics(cnv, [M1,M2,M3])
#Save the result as a DXF file
renderer.renderDXF(cnv, 'NonSeq.dxf')

---
Why did I create this ?

---
Many Constraints

---
Many Constraints

---
Optical Distance

---
Mode Matching
ROC Error Tolerance

---
POX

---
Unwanted
POX